Annexe 1

Code du module «Pedale»
 distortionSensorsV2.ino

/********************************************************************* / *********** distortion Effect for the MovingTones pedal ********** / *********** made by the MovingTones team ********** / *********** website :) ********** / * Licensed under a Creative Commons Attribution 3.0 Unported License * / ********************************************************************** / *********** effect adapted from the distortion effect by *********** / *********** www.electrosmash.com/pedalshield ********** / *********** Based on rcarduino.blogspot.com previous work ********** / **********************************************************************/ / /* To make this code compile you will need the following libraries: / * Adafruit_ST7735 / * Adafruit_GFX / * SPI.h / * EEPROM.h */ / // Libraries / #include "EEPROM.h" // / #include <Adafruit_GFX.h> // Core graphics library / #include <Adafruit_ST7735.h> // Hardware-specific library / #include <SPI.h> // Used during debugging to show messages on the Serial print / // Variables from the original effects' code / int in_ADC0, in_ADC1; // variables for 2 ADCs values (ADC0, ADC1) / int POT0, POT1, POT2, out_DAC0, out_DAC1; // variables for 3 pots (ADC8, ADC9, ADC10) / const int LED = 3; // LED in pin 3 / const int FOOTSWITCH = 7; // Footswitch in pin 7 / const int TOGGLE = 2; // Toggle in pin 2 / int upper_threshold, lower_threshold; // Variable for the distortion effect / const int SAVE_BUTTON = 1; // pins of the arduino / const int TFT_CS = 10; / const int TFT_RST = 8; / const int TFT_DC = 9; / Adafruit_ST7735 tft = Adafruit_ST7735(TFT_CS, TFT_DC, TFT_RST); // instantiate the screen / // New variables / const int STANDBY1_MODE = 0; // effects will only be applied when the pedal's footswitch is on HIGH / const int BUTTON_MODE = 1; // sequence of pressing produces: low-high-low-high or high-low-high-low / const int STANDBY2_MODE = 2; // if initially footswitch is HIGH, we will go to BUTTON_MODE / const int SENSOR_MODE = 3; // if intiially footswitch is LOW, we will go to STANDBY1_MODE / const int DEBOUNCE_DELAY = 50; // delay to be applied to debounce / const int MIN = 0; // range of the parameters p0, p1, p2 for the effects' code / const int MAX = 4096; / const int MIN_SCREEN = 0; // length of the bar graph to be displayed on the screen / const int MAX_SCREEN = 115; / const int MAX_POT = 4096; // readings from the bottons will be scaled to this range / const int MIN_POT = 0; / const int LIMIT_POT = 4096; / const int MAX_SENSORS = 180; // sensors send angles in this range throught the XBees / const int MIN_SENSORS = 0; / int footswitch_detect; // variables to fascilitate the toggle / int footswitch_detect_last; / int footswitch_detect_previous; / int save_button_detect; // currently not used / int save_button_press_time; / boolean save_button_pressed; / int footswitch_mode = STANDBY1_MODE; // instantiate footswitch_mode to STANDBY1_MODE / int last_debounce_time = 0; // variables to fascilitate debouncing / int last_update_time = 0; / int p0 = 0, p1 = 0, p2 = 0; // parameters to be used by the code to apply effects accordingly / int p0_old, p1_old, p2_old; / int MEMORYPOTMOD0 = 0, MEMORYPOTMOD1 = 0, MEMORYPOTMOD2 = 0; / // Variables needed for the comunication with the ArduinoNano who is sending information in Serial Port / byte incomingByte; //Bytes that are going to be used to add them and to see if there is any header between they two. / byte lastByte; // This will be just the byte before incomingByte / // Variables to assemble 16-bits ints from bytes received form the Arduino Nano through the XBees / // !!! Note that int on an Arduino DUE is 32-bit but in many other smaller Arduinos it is 16-bit / // Thus to avoid negative-wrapping-around-to-positive, use int16_t for all int variables in this program / int16_t currentInt; / int16_t int1; / byte byteArray[3]; / int16_t angles[3]; // the three angles read by the sensor as received from XBees / int16_t mask; / void setup() / { / //Configuration from the original effect from pedalShield / //ADC Configuration / ADC->ADC_MR |= 0x80; // DAC in free running mode. / ADC->ADC_CR = 2; // Starts ADC conversion. / ADC->ADC_CHER = 0xFFFF; // Enable all ADC channels / //DAC Configuration / analogWrite(DAC0, 0); // Enables DAC0 / analogWrite(DAC1, 0); // Enables DAC1 / // We are going to read from the FootSwitch to make our 3 modes. / pinMode(FOOTSWITCH, INPUT); // Enables to read from the footswitch / // pinMode(SAVE_BUTTON, INPUT); / pinMode(LED, OUTPUT); / // record the state of the footswitch when turned on / /*HERE WE SHOULD DETECT IF HI IS ALEREADY IN BYPASSMODE OR NOT. AND THEN START FROM HIS ORIGINAL STATE / *******************************************************************************************************/ / footswitch_mode = digitalRead(FOOTSWITCH); / footswitch_detect_last = digitalRead(FOOTSWITCH); / footswitch_detect_previous = footswitch_detect_last; / //Screen (add description and comments) / tft.initR(INITR_BLACKTAB); / tft.fillScreen(ST7735_BLACK); / // Here we set the screen parameters: orientation, text size, color and text display / tft.setRotation(-1); / tft.setTextSize(2); / tft.fillScreen(ST7735_WHITE); / tft.setTextColor(ST7735_RED); / tft.println("*Distortion*"); / tft.println(""); / tft.println(" P1"); / tft.println(""); / tft.println(" P2"); / tft.println(""); / tft.println(" P3"); / p0_old = p0; / p1_old = p1; / p2_old = p2; / // Initialize the Serial ports for message transmissions / Serial.begin(57600); //Initialize the port for comunication with the PC to send messages useful for coding (Serial) / Serial1.begin(57600); //Initialize the port for comunication with the XBee (Serial1) / // From XBee / lastByte = (byte)0; // We inicialize the lastBythe with 0 so it can make its first comparison. / } / void loop() / { / readFootSwitch(); //We read the FootWwitch State and we see if it's pressed. / updateScreen(); //We upload the screen information / // readSaveButton(); / // From the original effect code / // Read the ADCs / while ((ADC->ADC_ISR & 0x1CC0) != 0x1CC0); // wait for ADC 0, 1, 8, 9, 10 conversion complete. / in_ADC0 = ADC->ADC_CDR[7]; // read data from ADC0 / in_ADC1 = ADC->ADC_CDR[6]; // read data from ADC1 / // POT0=ADC->ADC_CDR[10]; // read data from ADC8 / // POT1=ADC->ADC_CDR[11]; // read data from ADC9 / // POT2=ADC->ADC_CDR[12]; // read data from ADC10 / // Changing the parameters values depending of the mode / switch (footswitch_mode) { / case STANDBY1_MODE: / case STANDBY2_MODE: / Serial.print("Standby Mode "); / break; / case BUTTON_MODE: / Serial.print("Button Mode: "); / readPotentiometer(); / break; / case SENSOR_MODE: / Serial.print("Sensor Mode: "); / readSensor(); / break; / default: / Serial.print("Invalid state "); / } / // We display the parameters values on the computer screen / Serial.print(p0); / Serial.print("|"); / Serial.print(p1); / Serial.print("|"); / Serial.print(p2); / Serial.print("|"); / Serial.println(""); / // Code for the effect 'distortion' - distortion does not use parameter p1 / // Code from the original effect: This is the effect, taking the parameters p0, p1 and p2 / upper_threshold = map(p0, 0, 4095, 4095, 2047); / lower_threshold = map(p0, 0, 4095, 0000, 2047); / if (in_ADC0 >= upper_threshold) in_ADC0 = upper_threshold; / else if (in_ADC0 < lower_threshold) in_ADC0 = lower_threshold; / if (in_ADC1 >= upper_threshold) in_ADC1 = upper_threshold; / else if (in_ADC1 < lower_threshold) in_ADC1 = lower_threshold; / //adjust the volume with POT2 / out_DAC0 = map(in_ADC0, 0, 4095, 1, p2); / out_DAC1 = map(in_ADC1, 0, 4095, 1, p2); / //Write the DACs / dacc_set_channel_selection(DACC_INTERFACE, 0); //select DAC channel 0 / dacc_write_conversion_data(DACC_INTERFACE, out_DAC0); //write on DAC / dacc_set_channel_selection(DACC_INTERFACE, 1); //select DAC channel 1 / dacc_write_conversion_data(DACC_INTERFACE, out_DAC1); //write on DAC / } / // reading the FOOTSWITCH on the pedalShield and implement a debouncing mechanism / void readFootSwitch() { / footswitch_detect = digitalRead(FOOTSWITCH); / if (footswitch_detect != footswitch_detect_last) { / last_debounce_time = millis(); / } / if (footswitch_detect != footswitch_detect_previous && millis() - last_debounce_time > DEBOUNCE_DELAY) { / footswitch_mode = (footswitch_mode + 1) % 4; / footswitch_detect_previous = footswitch_detect; / } / footswitch_detect_last = footswitch_detect; // we detect changes in the FOOTSWITCH by comparing these two variables / } / void readSaveButton() { / save_button_detect = digitalRead(SAVE_BUTTON); / if (save_button_detect == HIGH) { / last_debounce_time = millis(); / if (save_button_pressed = true) { / if (millis() - save_button_press_time > 3000) { / EEPROM.write(0, p0); / EEPROM.write(1, p1); / EEPROM.write(2, p2); / } else { / p0 = EEPROM.read(0); / p1 = EEPROM.read(1); / p2 = EEPROM.read(2); / } / save_button_pressed = false; / } / } / if (save_button_detect == LOW && millis() - last_debounce_time > DEBOUNCE_DELAY && save_button_pressed == false) { / save_button_press_time = millis(); / save_button_pressed = true; / } / } / void readPotentiometer() { / int POTMOD0 = ADC->ADC_CDR[2]; //reading first potentiometer / POT0 = updatePot(POT0, MEMORYPOTMOD0, POTMOD0); //update first parameter using current reading of potentiometer / p0 = POT0; //update globally / MEMORYPOTMOD0 = POTMOD0; //now the potentiometer reading becomes the 'previous' reading / //Serial.println(p0); / int POTMOD1 = ADC->ADC_CDR[1]; //read from pot1 //reading second potentiometer / POT1 = updatePot(POT1, MEMORYPOTMOD1, POTMOD1); //update second parameter using current reading of potentiometer / p1 = POT1; //update globally / MEMORYPOTMOD1 = POTMOD1; //now the potentiometer reading becomes the 'previous' reading / int POTMOD2 = ADC->ADC_CDR[0]; //read from pot2 //reading third potentiometer / POT2 = updatePot(POT2, MEMORYPOTMOD2, POTMOD2); //update third parameter using current reading of potentiometer / p2 = POT2; //update globally / MEMORYPOTMOD2 = POTMOD2; //now the potentiometer reading becomes the 'previous' reading / } / int updatePot(int POT, int MEMORYPOTMOD, int POTMOD) { //update the given parameter / int VALUE = 0; //Value to be added to previous values of parameters / if ((POTMOD - MEMORYPOTMOD) < -0.9 * MAX_POT) { // case of more than one complete turn in the positive direction / VALUE = MAX_POT + POTMOD - MEMORYPOTMOD; / if ((POT + VALUE) > LIMIT_POT) { / POT = LIMIT_POT; / } / else { / POT = POT + VALUE ; / } / } / else if ((POTMOD - MEMORYPOTMOD) > 0.9 * MAX_POT) { // case of more than one complete turn in the negative direction / VALUE = - (MAX_POT) + POTMOD - MEMORYPOTMOD; / if ((POT + VALUE) < MIN_POT) { / POT = MIN_POT; / } / else { / POT = POT + VALUE ; / } / } / else if ((POTMOD - MEMORYPOTMOD) > 0) { //case of less than one complete turn in the positive direction / VALUE = POTMOD - MEMORYPOTMOD; / if ((POT + VALUE) > LIMIT_POT) { / POT = LIMIT_POT; / } / else { / POT = POT + VALUE ; / } / } / else if ((POTMOD - MEMORYPOTMOD) < 0) { //case of less than one complete turn in the negative direction / VALUE = POTMOD - MEMORYPOTMOD;//+POTSENSOR / if ((POT + VALUE) < MIN_POT) { / POT = MIN_POT; / } / else { / POT = POT + VALUE ; / } / } / return POT; / } / // Read the 3 angles transmitted by the XBees if there is message available / // The 3 angles (6 bytes) are always sent together following an int header == -21846 / void readSensor() { / if (Serial1.available()) { / boolean header = false; // before a valid header is detected, header is set to false / lastByte = Serial1.read(); // read one byte / while (Serial1.available() && !header) { / incomingByte = Serial1.read(); // read another byte / int1 = assembleInt(lastByte, incomingByte); // each int is 16-bit, so we assemble the incoming int by applying bit-wise operations on the two bytes / // Serial.println("waiting"); // uncomment this line to see how long it takes to clear the buffer / if (int1 == -21846) { / header = true; // a correct header is detected / } / else { / lastByte = incomingByte; // if there is not any header we take our second byte as our first byte, to then make a comparison with the following / } / } / // if the header is detected, the next 6 bytes are the 3 values of the angles (each int is 16-bit) / readAngles(); / } / } / // assemble an int from the two bytes just read into byteArray / int16_t assembleInt(byte byte1, byte byte2) { / currentInt = (int16_t)byte1 << 8; / mask = 0xFF; / mask = mask & (int16_t)byte2; // mask the first 8 bit to zero, in case the byte is sign-extended / currentInt = currentInt | mask; / // the byte1*256 + byte2 before is wrong because byte2 had been sign-extended - have to mask the first 8 bits / //mask = 0xFF; / //currentInt = byte1*256 + (byte2 & mask); / return currentInt; / } / // Read the angles from the next 6 bytes (2 bytes for each 16-bit int angle) / void readAngles() { / // Expect 3 angles / for (int i = 0; i < 3; i++) { / /* We know that we should have a message in the buffer, (because we have reconized an header) / but, it can happen that the pedal tries to read the angles form the Serial before the sensor / manage to send him the angles (it can also be because of the data transmission speed v/s / the pedal's processor speed) / so here we wait for the next message if it's necessary / TODO: Use a timout!!*/ / while (!Serial1.available()) { / Serial.println("----Im waiting111111-"); / } / byteArray[0] = Serial1.read(); // We read the fist byte / while (!Serial1.available()) { // We wait again in case it is necesary TODO: Use a timout!! / Serial.println("----Im waiting222222-"); / } / byteArray[1] = Serial1.read(); // We read the second byte / angles[i] = assembleInt(byteArray[0], byteArray[1]); // We construct the angle using both bytes / } / /*Sometimes, (and I don't know yet why.. and this is a ToDo:try to prevent this from another way) / there are some messages that are eathier read badly or sended badly.. so we delete any message with an / incorrect angle*/ / if (angles[0] >= 0 && angles[0] <= MAX_SENSORS && angles[1] >= 0 && angles[1] <= MAX_SENSORS && angles[2] >= 0 && angles[2] <= MAX_SENSORS) { / // Writing the angles into the global variables / p0 = angles[0] * 4096 / MAX_SENSORS; //Here we scale the angle into our effect scale. here is until 4096 / p1 = angles[1] * 4096 / MAX_SENSORS; / p2 = angles[2] * 4096 / MAX_SENSORS; / } / } / void updateScreen() { / // only update the screen every 0.1 seconds / if (millis() - last_update_time > 100) { / last_update_time = millis(); / // if the new parameter is bigger than the old one, add a blue bar / // else add a white bar. this scheme is applied for every parameter. / if (p0_old < p0) { / tft.fillRoundRect(MIN_SCREEN, 32, map(p0, MIN, MAX, MIN_SCREEN, MAX_SCREEN), 16, 0, ST7735_BLUE); / } / if (p0_old > p0) { / tft.fillRoundRect(map(p0, MIN, MAX, MIN_SCREEN, MAX_SCREEN), 32, map(p0, MIN, MAX, MAX_SCREEN, MIN_SCREEN), 16, 0, ST7735_WHITE); / } / p0_old = p0; / if (p1_old < p1) { / tft.fillRoundRect(MIN_SCREEN, 64, map(p1, MIN, MAX, MIN_SCREEN, MAX_SCREEN), 16, 0, ST7735_BLUE); / } / if (p1_old > p1) { / tft.fillRoundRect(map(p1, MIN, MAX, MIN_SCREEN, MAX_SCREEN), 64, map(p1, MIN, MAX, MAX_SCREEN, MIN_SCREEN), 16, 0, ST7735_WHITE); / } / p1_old = p1; / if (p2_old < p2) { / tft.fillRoundRect(MIN_SCREEN, 96, map(p2, MIN, MAX, MIN_SCREEN, MAX_SCREEN), 16, 0, ST7735_BLUE); / } / if (p2_old > p2) { / tft.fillRoundRect(map(p2, MIN, MAX, MIN_SCREEN, MAX_SCREEN), 96, map(p2, MIN, MAX, MAX_SCREEN, MIN_SCREEN), 16, 0, ST7735_WHITE); / } / p2_old = p2; / } / }